Memo

To:	Operations Staff

From:	Larysa Prabakharan

Date:	April 16, 2014

Re:	Working With Asbestos

# Important

It is the policy of Shawma Construction Services Limited to comply fully with the requirements of the Control of Asbestos Regulations 2012.

Although surveys have shown that there is no asbestos on our own premises, site employees must all be aware of the management of asbestos regulations and should ask to see the register on arrival on site. No employees work with any Asbestos Contaminated Materials, and if there is any suspicion that Asbestos is evident work must cease immediately.

Should that be the case, an assessment report must be requested from the Client. If there does prove to be Asbestos present then specialist contractors will be employed to conduct the safe removal of materials in a controlled manner before employees are allowed back on site to continue work.

The following documents have been issued to all Operations staff:

- Shawma Construction Services Limited Asbestos Policy

- INDG289 Working with Asbestos in Buildings

If anybody has any doubts regarding working with Asbestos please refer to the written instructions within the guidance issued above.

Alternatively please speak to Managing Director if specific training is required.

WORKING WITH

ASBESTOS

IN BUILDINGS

Essential advice for

workers carrying out:

*Building maintenance

*Building repair

*Building refurbishment

Asbestos: The hidden killer!  Are you at risk?

*Building services

WORKING WITH ASBESTOS IN BUILDINGS

What does this leaflet tell you and who

is it for?

This leaflet tells you where you are most

likely to find asbestos and how to protect

yourself when working with it.  It will be

particularly useful for anyone involved in

building maintenance, repair or refurbishment

work, for instance, plumbers, carpenters and

electricians.  It will also be useful to other

workers, not normally associated with the

building trade; such as computer installers,

cabling installers, fire alarm installers and

telecommunications engineers, who may

also disturb asbestos during their work.

Safety representatives may also find this

leaflet useful.

2

WORKING WITH ASBESTOS IN BUILDINGS

What is asbestos?

There are three main types of asbestos - chrysotile, amosite

and crocidolite; they are usually called white, brown and blue

asbestos respectively.  However, they cannot be identified just

by their colour.

Blue and brown asbestos (the two most dangerous forms)

have not been imported into the UK for nearly 20 years and

their use was banned in 1985. White asbestos was banned

(except for a small number of specialised uses) in 1999.

What are the risks from asbestos?

Work with asbestos can release small fibres into the air.

Breathing in these fibres can eventually lead to a number of

fatal diseases.  These include:

asbestosis or fibrosis (scarring) of the lungs;

lung cancer; and

■

■

mesothelioma, a cancer of the inner lining of the

chest wall or abdominal cavity.

■

There is no cure for asbestos-related diseases.

Asbestos-related diseases are currently responsible for up to

3500 deaths a year in Britain.  There is usually a long delay

between first exposure to asbestos and the first symptoms of

disease.  This can vary between 15 and 60 years.  The vast

3

WORKING WITH ASBESTOS IN BUILDINGS

majority of those now dying were exposed to asbestos

between the 1950s and 1970s, before the current control

regulations were introduced.

It is possible that repeated low-level exposures may lead to

asbestos-related diseases, although high exposure for long

periods is linked more clearly to these illnesses.

But provided the asbestos material is intact and in a position

where it cannot easily be damaged, it will not pose a risk to

health by releasing fibres into the air.

Many of those suffering today from asbestos-related

diseases worked in the building trades.  They were

carpenters, joiners, shopfitters, plumbers, electricians,

gas service engineers etc.  They were exposed to

asbestos fibres in their day-to-day work with asbestos-

containing materials or because work with asbestos was

carried out near them.

4

WORKING WITH ASBESTOS IN BUILDINGS

How does asbestos get into the body?

Although the body will get rid of most of the larger fibres that

can enter the nose and mouth, tiny fibres can pass into the

lower parts of the lung.  They can stay there for years and in

some cases work their way through the lung lining.  The body

naturally gets rid of any asbestos fibres that you might take in

with food and water. Asbestos fibres cannot be absorbed

through your skin.

What types of buildings are likely to

contain asbestos?

Asbestos is likely to be in a building if :

it was built or refurbished between 1950 and 1980

and particularly;

■

if it also has a steel frame; and/or

■

it has boilers with thermal insulation.

■

But you also need to bear in mind that asbestos cement has

also been widely used as a building material since the 1950s.

5

WORKING WITH ASBESTOS IN BUILDINGS

Where is asbestos found in buildings?

Many thousands of tonnes of asbestos were used in buildings

in the past.  Much of this is still there and you cannot easily

identify it from its appearance.

Its most common uses were:

sprayed asbestos and asbestos loose packing -

generally used as fire breaks in ceiling voids;

■

moulded or preformed sprayed coatings and lagging -

generally used in thermal insulation of pipes and

boilers;

■

sprayed asbestos mixed with hydrated asbestos

cement - generally used as fire protection in ducts,

firebreaks, panels, partitions, soffit boards, ceiling

panels and around structural steel work;

■

insulating boards used for fire protection, thermal

insulation, wall partitions and ducts;

■

asbestos cement products, which can be compressed

into flat or corrugated sheets;  corrugated sheets are

largely used as roofing and wall cladding; other

asbestos cement products include gutters, rainwater

pipes and water tanks;

■

6

WORKING WITH ASBESTOS IN BUILDINGS

Steelwork coated with asbestos spray for fire protection.

The photograph also shows a section of asbestos lagged

pipework. The insulation on both has been partly removed.

A ceiling coated with asbestos spray, which has been damaged

by building work.

7

WORKING WITH ASBESTOS IN BUILDINGS

Typical locations where lagging might be found.

8

WORKING WITH ASBESTOS IN BUILDINGS

Atypical

asbestos

insulation board

ceiling.

A severely

damaged

wall

partition

made of

asbestos

insulating

board.

9

WORKING WITH ASBESTOS IN BUILDINGS

some reinforced plastics, mastics and sealant;

■

millboard, paper and paper products used for the

insulation of electrical equipment. Asbestos paper has

been used as a fireproof facing on wood fibreboard;

■

certain textured coatings, decorative plasters and paints;

■

asbestos ropes and cloth.

■

So what should you do?

Any asbestos-containing materials on site should have been

identified before work starts.  Those responsible for the building

have a legal requirement to provide your supervisor/employer

with information on the location and condition of these

materials. Work with asbestos insulation, asbestos coatings and

asbestos insulating board must normally be carried out by an

HSE-licensed contractor. Before you start work ask the building

manager or your supervisor 'Has the site been checked for

asbestos?' If there is asbestos and if you are likely to come into

contact with it, get advice from those in charge.  If you are in

any doubt about whether the material you are working with

contains asbestos, STOP WORK, and find out.

If you come across any hidden or dusty materials which you

suspect may contain asbestos, stop work and get advice. The

person in charge of the job must find out if there is any

asbestos on the site or assume that anything that looks like

asbestos is asbestos. Identification of asbestos-containing

materials is not easy and you can only be sure they are

asbestos if they have been tested by a specialist laboratory.

10

WORKING WITH ASBESTOS IN BUILDINGS

What should those in charge of

the job do?

They must:

decide whether or not the work needs to be carried

out by a specialist asbestos removal contractor;

■

assess the risk to your health from any work that you

do, and decide what precautions you need to take;

■

prevent your exposure to asbestos or reduce it to the

lowest level possible by using suitable controls,

banning the use of power tools, dampening the

material, enclosing the work and using dust extraction

equipment;

■

give you information, instruction and training so that

you know the risks and the precautions you should

take;

■

give you clean protective clothing to wear when you

work with asbestos;

■

make sure you are properly trained to use a

respirator (mask) if you need one, that you know how

to fit it properly and that it’s in good working order,

is clean and is stored in a safe place;

■

consult the health and safety representative, if there

is one, about the control measures to be taken.

■

11

WORKING WITH ASBESTOS IN BUILDINGS

What can you do to protect yourself?

Do:

keep the asbestos-containing materials damp while

you work on them;

■

use hand tools;

■

use the personal protective equipment given to you,

including a respirator (mask);

■

clean up as you go, don’t let waste pile up;

■

clear up asbestos dust using a special 'Type H'

vacuum cleaner or damp cloths;

■

wash your hands and face when you take a break,

and at the end of the day’s work;

■

put asbestos waste into a suitable sealed container.

You can use a heavy duty polythene bag, put that in a

second bag and then label it to show that it contains

asbestos (remember that, in most cases, asbestos

waste needs to be taken to a licensed tip).

■

12

WORKING WITH ASBESTOS IN BUILDINGS

Don’t:

use power tools - they create more dust;

■

take home to wash the overalls you have worn while

working with asbestos;

■

eat or drink in the work area;

■

smoke - the risk of lung cancer from asbestos is

higher among smokers.

■

DON’T FORGET

Be alert at all times to the dangers of working

with materials that may contain asbestos.  If

you come across asbestos - stop work and

tell your supervisor. Avoid exposure to all

dust.  Follow the advice in this leaflet and

protect your health and that of your

workmates.  Encourage them to do the same.

13

WORKING WITH ASBESTOS IN BUILDINGS

More information

You can also find out more about working with asbestos from

your safety representative, the nearest office of the Health and

Safety Executive, or your Local Authority Environmental Health

Department, which is listed in your telephone directory.

HSE guidance

A comprehensive guide to managing asbestos in premises

HSG227 HSE Books 2002 ISBN 0 7176 2381 5

Asbestos essentials task manual: Task guidance sheets for the

building and allied trades HSG210 HSE Books 2001

ISBN 0 7176 1887 0

Introduction to asbestos essentials: Comprehensive guidance

on working with asbestos in the building maintenance and

allied trades HSG213 HSE Books 2001 ISBN 0 7176 0901 X

HSE video

How are you managing? Dealing with the risks of asbestos in

buildings Video HSE Books 2004 ISBN 0 7176 2768 3

HSE free publications

Asbestos alert for building maintenance, repair and

refurbishment workers: Be aware of asbestos the hidden killer

Pocket card INDG188 HSE Books 1995 (single copy free or

priced packs of 25 ISBN 0 7176 1209 0)

Ashort guide to managing asbestos in premises Leaflet

INDG223(rev3) HSE Books 2002 (single copy free or priced

packs of 10 ISBN 0 7176 2564 8)

14

WORKING WITH ASBESTOS IN BUILDINGS

HSE priced and free publications are available by mail order

from HSE Books, PO Box 1999, Sudbury, Suffolk CO10 2WA

Tel: 01787 881165  Fax: 01787 313995 Website:

www.hsebooks.co.uk (HSE priced publications are also

available from bookshops and free leaflets can be down-

loaded from HSE’s website: www.hse.gov.uk).

For information about health and safety ring HSE's Infoline

Tel: 08701 545500 Fax: 02920 859260 e-mail:

hseinformationservices@natbrit.com or write to HSE

Information Services, Caerphilly Business Park, Caerphilly

CF83 3GG.

This leaflet is available in priced packs of 10 from HSE Books,

ISBN 0 7176 1697 5. Single copies are also available from

HSE Books.

15

WORKING WITH ASBESTOS IN BUILDINGS

This leaflet tells you where you are most likely to find

asbestos and how to protect yourself when working

with it.  It will be particularly useful for anyone

involved in building maintenance, repair or

refurbishment work, for instance, plumbers,

carpenters and electricians.  It will also be useful to

other workers, not normally associated with the

building trade; for instance computer installers,

cabling installers, fire alarm installers and

telecommunications engineers may also disturb

asbestos during their work. Safety representatives

may also find this leaflet useful.

This leaflet contains notes on good practice which are not compulsory

but which you may find helpful in considering what you need to do.

© Crown copyright  This publication may be freely reproduced,

except for advertising, endorsement or commercial purposes. First

published 4/99. Please acknowledge the source as HSE.

INDG289   Reprinted 10/04   C350

Printed and published by the Health and Safety Executive